Stantonbury Theatre

Technical Specifications

January 2019

Stage and Auditorium

Auditorium

Capacity raked seating: 198

Capacity including additional seating in pit: 250

Number of seats lost for mixer position in auditorium: min 10 (please see note below)

Stage Dimensions

Upstage edge of the pit (setting line) – Upstage wall			11.20 mtrs

Upstage edge of the pit (setting line) – Full blacks			7.70 mtrs

Width (Wall to wall – no masking)					15.20 mtrs

Width (with typical masking)						9.00 mtrs

Depth of pit								0.73 mtrs

Height to bars							5.35 mtrs

Stage floor – Flat, Sprung, Semi polished beech or black dance floor. Suitable for dance.

PLEASE BE AWARE THAT THE FRONT OF THE STAGE IS THE EDGE OF THE 3M ORCHESTRA PIT. 52 SEATS ARE SOLD IN HERE AFTER THE RAKED SEATING HAS REACHED CAPACITY, DUE TO REDUCED VISIBILITY OF THE FLAT SURFACE.

SCREWING OR FIXING TO THE STAGE FLOOR IS NOT PERMITTED AT ANY TIME

Drapes/Masking

Indigo blue velour house tabs on track. Electrically operated from control room or USL

Serge Full Black travelers US (7.7 mtrs from setting line) hand winch operated from USR

6x Black serge legs							2m x 5m

1x White cyclorama	(Permanently hung on back wall)		15m x 5m

1 x	Chauvet Sparklite LED Starcloth (rigged on back wall)

Rigging

All bars are 48mm O/D secured to girders, load limit of 30kg between node connections (3m length).

6x free standing boom bases to take 48mm OD Barrel.

Dock and Get-in

The dock doors are 3.68m x 1.7m at ground level opening into L shape dock area.

Parking at the dock door for touring van is permitted for unloading and the duration of your stay. There is ample free parking close by.

Staging

12 of 4’ x 4’ Litedeck with 1’, 2’ or 3’ legs

Black Harlequin dance floor

Lighting

House Lighting

GDS wireless DMX controlled 2 cell unit LED’s over auditorium, 4 cell over stage

Stage lighting

80 amp three phase supply

1 x ETC Ion Xe 20 lighting control console

72 x Hard wired 10 Amp Dimmers (ETC Smartpack)

5 x fixed position IWB, 12 way bars all with 15amp outlets. (See Plan for bar positions)

6 x 15amp outlet DIP circuits MSL

6 x 15amp outlet DIP circuits MSR

1 x 63 amp 3 phase Auxiliary power supply adjacent to the dock Door

Lantern stock

6 x                    ETC Source4 36o Profile 750W

1 x                    ETC Source4 19o Profile 750W

26 x                  CCT Starlette Fresnel                                         1 KW

2 x                    ADB Fresnel                                                     1 KW

8 x                    ETC Source4 Fresnel                                         750W

10 x                  ETC Source4 Zoom 15-30 Profile                       750W

5 x                    PAR64 Can (CP62)                                            1 KW

6 x                    Source four jr. 25-50 Profile                               575 w

8 x                    Source four par-EA                                           750 w

5 x                    Chauvet COLORado Batten 72 Tour LED Baton

6 x                    ETC Colour source par LED                               110W

4 x                    D.T.S. P36 Pinspot Short Eco 230v                   30W

4 x                    Selecon Lui Flood                                             1 KW

1 x                    Chauvet SparkliteLED Starcloth (rigged on back wall)

General L.X Equipment

Selection of TRS extension cabling.

NO Grelcos/splitters available at this time

A size and B size gobo holders for our CCT Freedom and Silhouette lanterns, M size for S4jr, A size for S4 Zooms and 19’s.

Sound & Communications

Natural acoustic suitable for music and spoken word.

Microphones

4x	Shure		SM-58		Cardioid microphone

4x   Shure		SM-57		Cardioid microphone

2x Studiospares large diaphragm condenser microphones

7x Active DI boxes

Playback

2x	Denon		DNC615	Compact Disc Player

1 x 	Tascam		MD350		Minidisc Player.

Sound

1x Allen and Heath 	QU-32 		Digital mixing console

1x Allen and Heath 	AR2412 	Digital audio rack

The above configuration gives 24 inputs and 12 outputs to stage

Amplification

1x Dynacord 	L1800FD 	(Main FOH PA)

1x Dynacord		L2800FD	(Main FOH PA)

1x Samson               Servo300           (Main Front Fill)

1x Yamaha		P1500 		(on-stage monitoring)

1x Samson Servo75			(control room monitoring)

Speakers

2x EV		ELX215 	(Main FOH PA)

2x EV 		ELX118 	(Main FOH PA)

2x JBL 		control 1 	(Main Front Fill)

2x EV 		SX300 		(on-stage monitoring)

2x Tannoy reveal control room monitors

We also have 4 JBL eon speakers available with suitable amplification. Please contact us if these are required.

Comms

4x	Tecpro/Metro Audio		     Comms belt packs with Single Muff Headset

No Cue Lights

Show relay to control room (NOT to dressing rooms)

- ic tie lines around stage terminating at patch bay at rear of control room.

12 speaker tie lines around stage at grid level. 6 at stage level terminating in patch bay at rear of control room

Audio Visual

There are currently no AV solutions available, please bring you own projectors and cabling should you need to use this for your shows.

Due to conditions imposed by the licensing authority, if an auditorium mixer position is required, it can only be located at the rear of the auditorium in front of the control room, a minimum of 10 seats are lost by doing this (often more depending on the size of the position.) We recommend mixing from the control room, we can easily remove the glass from the window to facilitate this.

Welfare

Facilities

There is a green room backstage that incudes, tea and coffee making facilities, fridge and a microwave. Patrons may need to provide their own consumables, if a rider is not part of your contract.

Ladies and gents toilets are also to be found in the backstage corridor.

Some dressing rooms have sinks in, all sinks (including in toilets) are supplied with drinking water.

Wardrobe

There is a washing machine and tumble dryer in the green room. There is also an iron and ironing board.

IF YOU REQUIRE ANY FURTHER INFORMATION PLEASE CONTACT THE TECHNICAL MANAGER - (01908) 324423 or email: theatre.tech@stantonbury.org.uk